## Slide 1
TYPING WITHOUT HANDS
CHONG JING HONG
U1922300B
Notes: Good afternoon, Professors.
My name is Jing Hong and I will be presenting my Final Year Project titled: Typing Without Hands

## Slide 2
Introduction
01
System Design & Analysis
02
Implementation
03
AGENDA
User Studies
04
Conclusion
05
Notes: This is the agenda for the presentation
I’ll start off with the introduction, and move on to the system design and analysis
Next, I will talk about the implementation of the project and the user studies conducted
Lastly, I will conclude the presentation

## Slide 3
The Past, Present And Future Of Messaging
By Andrea Giacomini
6 January 2021
“... 23 billion texts are sent worldwide each day — that’s 270,000 every second.”
  Typing - an important part of daily our lives
    Needed for work, communication etc.
BACKGROUND INFO & MOTIVATION
01 INTRODUCTION
  Not everyone can type with their hands
    People with Motor Neuron Diseases (MNDs)
    Need for alternative typing solution
Notes: Typing has become an important part of our daily lives, as it is required for various activities such as work, communication, education, and more.
According to Forbes, an estimated 270,000 texts were sent every second in 2021
Typing may be easy for many of us, but for people with medical conditions like motor neuron diseases, it may be difficult or even impossible to type using their hands.
Therefore, there is a need to develop an alternative system to allow these groups of people to type.

## Slide 4
  Eye typing
    Generate text using one’s gaze as an input mechanism
BACKGROUND INFO & MOTIVATION
  1. Measures the position of the user’s eyeballs, determines the point at which the user is looking
2. Gaze at the desired key, perform key selection
Hello World
3. Outputs selected key
01 INTRODUCTION
Notes: One possible way is through eye typing.
Eye typing is a method of generating text through the use of one’s gaze as an input mechanism
[CLICK]
In most eye typing systems,
[CLICK]
an eye tracking device measures the position of the user’s eyeballs and determines the point at which the user is looking.
[CLICK]
To select a key, the users gaze at the desired key on an onscreen keyboard and performs a key selection.
[CLICK]
The eye typing system detects the key selection and outputs the selected key

## Slide 5
PROJECT OBJECTIVES
Develop a low-cost system capable of eye tracking and gaze estimation using a webcam
01
02
03
Design a novel virtual keyboard that can tolerate inaccuracies in eye tracking and gaze estimation
Conduct user studies that compare the performance of the novel keyboard against the QWERTY keyboard.
01 INTRODUCTION
Notes: With that in mind, these are the objectives of the project
[CLICK]
The first objective is to develop a low-cost system capable of eye tracking and gaze estimation using a webcam.
[CLICK]
The second objective is to design a novel virtual keyboard that can tolerate inaccuracies from eye tracking and gaze estimation.
[CLICK]
The final objective is to conduct user studies that compare the performance of the novel keyboard against the QWERTY keyboard to evaluate the usability and effectiveness of the new system. The evaluation metrics are:
The typing speed
the typing accuracy
and the overall user satisfaction.

## Slide 6
02 SYSTEM DESIGN & ANALYSIS
EYE TYPING SYSTEM
  Appearance-based
    use the photometric appearance of the eyes to detect and track them
  Highly performant under different environmental conditions
  Google’s MediaPipe FaceMesh
Eye Tracking
Gaze Estimation
Key Selection
  Appearance-based
    estimate the gaze direction based on the appearance of the eye
  Standard machine learning algorithms
    Short training time with high accuracies
  Drawbacks:
    Fixed head pose – enforced through chin rest
  Dwell selection
  Balance between accuracy and ease of implementation
Notes: Moving on to the system design and analysis of eye typing system, I’ve split the eye typing system into 3 components:
Eye tracking
Gaze Estimation
Key selection
[CLICK]
For eye tracking, an appearance-based technique was used. Appearance-based eye tracking use photometric appearance of the eyes to detect and track them. This is because appearance-based eye tracking is highly performant under different environmental conditions, making it more accurate than the other approaches. In this project, Google’s MediaPipe FaceMesh was utilized for this purpose.
[CLICK]
For gaze estimation, I opted for an appearance-based technique that utilized standard machine learning algorithms. This was mainly due to the algorithms having minimal training time but yielding high accuracies. However, one drawback of this approach is that it requires a fixed head pose, which I enforced by using a chin rest.
[CLICK]
The dwell selection method was chosen as the key selection method. This is because it provides a good balance between accuracy and ease of implementation.

## Slide 7
02 SYSTEM DESIGN & ANALYSIS
EYE TYPING SYSTEM
EYE TRACKING
  Method: Appearance-based
    Use the photometric appearance of the eyes to detect and track them
  Highly performant under different environmental conditions
  Google’s MediaPipe FaceMesh
Notes: Moving on to the system design and analysis of eye typing system, I’ve split the eye typing system into 3 components:
Eye tracking
Gaze Estimation
Key selection
[CLICK]
For eye tracking, an appearance-based technique was used. Appearance-based eye tracking use photometric appearance of the eyes to detect and track them. This is because appearance-based eye tracking is highly performant under different environmental conditions, making it more accurate than the other approaches. In this project, Google’s MediaPipe FaceMesh was utilized for this purpose.
[CLICK]
For gaze estimation, I opted for an appearance-based technique that utilized standard machine learning algorithms. This was mainly due to the algorithms having minimal training time but yielding high accuracies. However, one drawback of this approach is that it requires a fixed head pose, which I enforced by using a chin rest.
[CLICK]
The dwell selection method was chosen as the key selection method. This is because it provides a good balance between accuracy and ease of implementation.

## Slide 8
02 SYSTEM DESIGN & ANALYSIS
EYE TYPING SYSTEM
GAZE ESTIMATION
  Method: Appearance-based
    Estimates the gaze direction based on the appearance of the eye captured by a model
  Standard machine learning algorithms
    Short training time with high accuracies
  Drawbacks:
    Fixed head pose – enforced through chin rest
Notes: Moving on to the system design and analysis of eye typing system, I’ve split the eye typing system into 3 components:
Eye tracking
Gaze Estimation
Key selection
[CLICK]
For eye tracking, an appearance-based technique was used. Appearance-based eye tracking use photometric appearance of the eyes to detect and track them. This is because appearance-based eye tracking is highly performant under different environmental conditions, making it more accurate than the other approaches. In this project, Google’s MediaPipe FaceMesh was utilized for this purpose.
[CLICK]
For gaze estimation, I opted for an appearance-based technique that utilized standard machine learning algorithms. This was mainly due to the algorithms having minimal training time but yielding high accuracies. However, one drawback of this approach is that it requires a fixed head pose, which I enforced by using a chin rest.
[CLICK]
The dwell selection method was chosen as the key selection method. This is because it provides a good balance between accuracy and ease of implementation.

## Slide 9
02 SYSTEM DESIGN & ANALYSIS
EYE TYPING SYSTEM
KEY SELECTION
  Method: Dwell Selection
    Key is selected if user’s gaze is fixated on it for more than some predetermined time
  Balance between accuracy and ease of implementation
Notes: Moving on to the system design and analysis of eye typing system, I’ve split the eye typing system into 3 components:
Eye tracking
Gaze Estimation
Key selection
[CLICK]
For eye tracking, an appearance-based technique was used. Appearance-based eye tracking use photometric appearance of the eyes to detect and track them. This is because appearance-based eye tracking is highly performant under different environmental conditions, making it more accurate than the other approaches. In this project, Google’s MediaPipe FaceMesh was utilized for this purpose.
[CLICK]
For gaze estimation, I opted for an appearance-based technique that utilized standard machine learning algorithms. This was mainly due to the algorithms having minimal training time but yielding high accuracies. However, one drawback of this approach is that it requires a fixed head pose, which I enforced by using a chin rest.
[CLICK]
The dwell selection method was chosen as the key selection method. This is because it provides a good balance between accuracy and ease of implementation.

## Slide 10
EYE TYPING SYSTEM
FUNCTIONAL REQUIREMENTS
  Detect users’ eyes and track their positions in real time.
  Estimate where users are gazing and move the cursor accordingly in real time.
  Detect if a key has been selected via dwell selection.
  Record all the keys selected by users and display the transcribed text.
NON-FUNCTIONAL REQUIREMENTS
  Run steadily at 30 frames per second, to ensure a smooth user experience.
  Chin rest must be at an appropriate height and distance away from the display so that users can see the whole screen.
  Chin rest must be comfortable for users to rest their chins.
02 SYSTEM ANALYSIS & DESIGN
Notes: These are the functional requirements of the eye typing system:
The eye typing system must….
[CLICK]
Next, these are the non-functional requirements of the eye typing system:
The eye typing system must

## Slide 11
NOVEL KEYBOARD
FUNCTIONAL REQUIREMENTS
  Have larger-than-normal keys.
    To compensate for inaccuracies in eye tracking and gaze estimation
  Keys are selectable via dwell selection.
  Outputs the correct key or function.
  Feedback to tell users the amount of dwell time left and where the cursor is hovering.
  Have the following keys:
    Numbers (0 - 9)
    Uppercase and lowercase letters
    Special characters (!@#$%^&*()-=_+[]\{}|;’:”,./<>?)
    Delete
    Enter
    Shift
    Space
02 SYSTEM ANALYSIS & DESIGN
Notes: These are the functional requirements of the LTNK keyboard:
The keyboard must…

## Slide 12
NOVEL KEYBOARD
NON-FUNCTIONAL REQUIREMENTS
  Intuitive layout
    Users must be able to understand what each button does without explanation
  Users must be able to see the output of the key selection immediately.
02 SYSTEM ANALYSIS & DESIGN
Notes: These are the non-functional requirements of the LTNK keyboard:
The keyboard must…

## Slide 13
NOVEL KEYBOARD - LTNK KEYBOARD
Level One
Level Two
02 SYSTEM ANALYSIS & DESIGN
  Displays the keyboard keys that are grouped together
  Displays individual keys for more detailed input
Notes: This is the design of the novel keyboard called LTNK keyboard. The LTNK keyboard features a two-level hierarchical design.
[CLICK]
The level one page displays the keyboard keys that are grouped together
[CLICK]
while the level two pages display individual keys for more detailed input.
[CLICK]
To facilitate ease of use, five larger buttons are present on all pages.
[CLICK]
These buttons are the ‘...’ back button, shift button, delete button, enter button, and space button.
[CLICK]
Alphabetic and numeric keys are arranged in order while special character keys are grouped based on their proximity to each other on the QWERTY keyboard layout.
[CLICK]
The LTNK keyboard also provides visual feedback to users whenever a key has been selected or is unavailable to use by highlighting the keys in grey and red respectively.

## Slide 14
HARDWARE REQUIREMENTS
MacBook Air (2020)
Apple M1 processor
16GB memory
macOS Ventura 13.2.1
720p FaceTime HD camera
13.3-inch display
Chin Rest
Shoebox of height 11.1cm
Book of height 3.4cm
Book of height 2.4cm
02 SYSTEM ANALYSIS & DESIGN
Notes: These are the hardware resources used for this project

## Slide 15
SOFTWARE REQUIREMENTS
Python
Version 3.9.15
PYNPUT
PACKAGES
02 SYSTEM ANALYSIS & DESIGN
Notes: These are the software resources that were used.
The project was coded in Python and to the right are all the Python packages that were used

## Slide 16
03 IMPLEMENTATION
EYE TRACKING
  OpenCV
    Capture images continuously from webcam
  MediaPipe FaceMesh
    Process images, detect facial landmarks
    468 facial landmarks, including eye centres
Notes: I will now delve into the implementation of the eye typing system
[CLICK]
For the eye tracking, a combination of OpenCV and Google’s MediaPipe FaceMesh were used.
Using OpenCV, images are captured continuously from the laptop webcam.
[CLICK]
The captured images are then processed by FaceMesh, whereby a total of 468 facial landmarks will be detected, including the centres of the left and right eyes.

## Slide 17
EYE TRACKING
Tracking point
03 IMPLEMENTATION
Notes: The middle point between the centres of the left and right eyes was used as the tracking point for the eye typing system. The point was calculated by averaging the x and y coordinates of the two eye centres.

## Slide 18
GAZE ESTIMATION - RELATING TRACKING POINT TO GAZE POINT
LINEAR RELATIONSHIP
03 IMPLEMENTATION
Notes: To develop the gaze estimation model, a preliminary study was conducted to establish a relationship between the tracking point and the gaze point.
[CLICK]
9 gaze points were plotted on the computer screen and each point was sequentially gazed at. The coordinates of the tracking point were recorded at each gaze.
To ensure consistency in the head pose, the chin rest was used to support my head and prior to each recording, the tracking point was aligned with p5. For each gaze points, 20 tracking point coordinates were recorded.
[CLICK]
The tracking points were then plotted out using the Matplotlib package and the results are shown on the right. Looking at both images, it is evident that the plots of the tracking point align with the gaze points.
[CLICK]
This linear alignment indicates that a linear relationship exists between the tracking point and the gaze points.

## Slide 19
  Collect more data
    16 additional gaze points
    Generate a random gaze point every 10 seconds within each grid, 20 per grid
    Total of 680 tracking points collected
GAZE ESTIMATION - DATA COLLETION
03 IMPLEMENTATION
Notes: Having established a linear relationship between the tracking point and gaze points, linear regression model can be constructed.
To collect more data, 16 additional gaze points were plotted on the computer screen and the same process of recording the coordinates of the tracking point while looking at each of these new gaze points was repeated.
Additionally, a script was developed to generate a random gaze point every 10 seconds within each grid. For each grid, 20 random gaze points were generated.
A total of 680 tracking point coordinates were recorded.

## Slide 20
GAZE ESTIMATION - LINEAR REGRESSION MODEL
  Scikit-Learn library's linear regression model
    X – mean tracking point coordinates
    Y - gaze coordinates
03 IMPLEMENTATION
Notes: To generate the gaze estimation model, the mean of coordinates of the tracking point for each gaze point were calculated.
The Scikit-Learn library's linear regression model was then utilised to fit the tracking point coordinates as the X parameter and the gaze coordinates as the Y parameter

## Slide 21
GAZE ESTIMATION - LINEAR REGRESSION MODEL
  Model Accuracy
    R score - 0.953
    Plot the graphs of tracking point coordinates against both the actual gaze coordinates and the model-predicted gaze coordinates
2
03 IMPLEMENTATION
Notes: To evaluate the accuracy of the gaze estimation model, the R2 score was calculated.
The R2 score value was 0.953, indicating a high accuracy
The graphs of the tracking point coordinates against both the actual gaze coordinates and the model-predicted gaze coordinates were also plotted. The plots shows that the two graphs closely align, indicating a strong match between the model estimates and the actual data.

## Slide 22
LTNK KEYBOARD
03 IMPLEMENTATION
Notes: To develop the LTNK keyboard, an object-oriented programming approach was used.
The figure on the left shows the class diagram of the LTNK keyboard. The LTNK keyboard class comprises of various button classes and has functions to switch between keyboard pages and output key selections
The figure on the right shows the keyboard. Each key has a progress bar to indicate the progress of the dwell selection. The yellow dot in the middle indicates the centre of the screen and serves as a reference point for users to maintain their head pose

## Slide 23
GUI
Keyboard situated in the centre
Display for selected keys
03 IMPLEMENTATION
Notes: This is the GUI of the eye typing system.
The top white bar displays the output of the selected keys
The keyboard is situated in the center of the screen

## Slide 24
04 USER STUDIES
SETUP
  Same setup is used for all user studies
  Data collected:
    Sequence of typing prompts
    Sequence of participants' inputs
    Time taken to eye type each input
Notes: I will now discuss the user studies conducted. Four user studies were conducted in total.
The same experimental setup was used for all user studies conducted.
The data collected in all experiments included the sequence of typing prompts, the participants’ inputs, and the time taken to eye type each input.

## Slide 25
01 USER STUDIES
i. DETERMINING APPROPRIATE DWELL TIME
OBJECTIVES
  Determine the appropriate dwell time for comparing the QWERTY and LTNK keyboards
  Appropriate if:
    Average typing accuracies: [85%, 100%]
    Accuracies are within 5% of each other
Notes: The first user study was conducted to determine the appropriate dwell time to use for comparing the QWERTY and LTNK keyboards
In this experiment, a dwell time is considered appropriate if:
The typing accuracies using the dwell time is between 85-100%
And the accuracies are within 5% of each other

## Slide 26
04 USER STUDIES
METHOD
  Dwell times tested: 800ms, 500ms and 400ms
  Order:
    QWERTY, LTNK
    800ms, 500ms, 400ms
  Two phases:
    Practice - Get familiar with eye typing with the corresponding dwell time
    Test - Eye type a set of 20 characters as fast and accurate as possible
i. DETERMINING APPROPRIATE DWELL TIME
Notes: In this study, dwell times of 800, 500 and 400ms were tested
All participants performed the user study in the same order, starting with the QWERTY keyboard followed by the LTNK keyboard, with the dwell time descending from 800ms to 400ms for both keyboards.
Each dwell time was divided into two phases: a practice phase and a test phase.
The practice phase is a 10 minutes practice session where participants get familiar with eye typing with the corresponding dwell time.
In the test phase, participants were required to eye type, as quickly and accurately as possible, a set of 20 characters that were displayed one after another.

## Slide 27
04 USER STUDIES
i. DETERMINING DWELL TIME TO USE
RESULTS
Notes: These are the results of the user study
As dwell time decreased, the typing accuracy for both keyboards decreased.
A shorter dwell time causes the ‘Midas Touch Problem’ where every key a user gazes at becomes a selection, even if the user was moving across the keyboard to find the desired key to select.
In general, the typing accuracy of the QWERTY keyboard is lower than that of the LTNK keyboard. This is because the QWERTY keyboard has smaller keys and more keys in a given area than the LTNK keyboard. This causes more errors to occur in typing as the gaze estimation model cannot accurately distinguish between the gaze coordinates for the intended key and the neighbouring keys.
[CLICK]
From the results, we can conclude that the most appropriate dwell time to use for the remaining user study is 800ms as typing accuracies for keyboards are within the range of 85% to 100% and are within 5% of each other. All user studies conducted subsequently used an 800ms dwell time.

## Slide 28
04 USER STUDIES
ii. IMPROVING NAVIGATION EFFICIENCY OF LTNK
OBJECTIVES
  Improve navigation between adjacent level two pages
    Initial design incurs a two-button selection penalty
    Add two carousel buttons on each level two page, reduce penalty to one-button
Notes: The initial design of the LTNK keyboard incurred a two-button selection penalty between adjacent level two pages.
In order to reduce the switching cost between adjacent level two keyboard pages, a design variation was proposed to include two carousel buttons on each level two page. This would reduce the penalty to just one button
Hence, the 2nd study was conducted to test if this design modification helped to switching time between adjacent level two keyboards and in turn increase typing speed.

## Slide 29
04 USER STUDIES
ii. IMPROVING NAVIGATION EFFICIENCY OF LTNK
METHODS
  Users split into two groups: Group A and Group B
    A - Initial Design first, New Design second
    B - New Design first, Initial Design second
  Two phases for each design:
    Practice - Get familiar with eye typing with the corresponding dwell time
    Test - Eye type a set of 20 characters as fast and accurate as possible
      Each set of characters required users to make the same keyboard page switches
Notes: Complete counterbalancing was used to prevent any order effects
The participants were split into 2 groups A and B
Group A performed the tests with the initial design first, new design second
Group B performed the test in the opposite order
Like the previous user study, there were two phases: practice and test
In the test phase, Each set of characters required users to make the same keyboard page switches

## Slide 30
04 USER STUDIES
ii. IMPROVING NAVIGATION EFFICIENCY OF LTNK
Design 1 - Initial design
Design 2 - New design
RESULTS
Notes: These are the results of the experiment
[CLICK]
It is evident that the new design achieved faster switching time between adjacent level two pages for all participants
This indicates that the design modification effectively reduces the time taken to switch between adjacent level two pages and improves the overall speed of eye typing on the LTNK keyboard.
As a result, the LTNK keyboard will adopt the new design and this new design will be utilized in next user studies.

## Slide 31
04 USER STUDIES
iii. LTNK KEYBOARD VS QWERTY KEYBOARD
OBJECTIVES
  Compare users’ typing performance when using the LTNK keyboard and the QWERTY keyboard
VS
Notes: The third user study compares users’ typing performance when using the LTNK keyboard and the QWERTY keyboard. The metrics evaluated were users’ typing speed, typing accuracy and overall user satisfaction.

## Slide 32
04 USER STUDIES
iii. LTNK KEYBOARD VS QWERTY KEYBOARD
METHODS
  Users split into two groups: Group A and Group B
    A - QWERTY first, LTNK second
    B - LTNK first, QWERTY second
  Two phases for each keyboard:
    Practice - Get familiar with eye typing with the corresponding dwell time
    Test - Eye type a set of 20 characters as fast and accurate as possible
      Pattern of five keys that were far apart from each other, followed by five keys that were next to each other, alternating
  Participants filled up a Google Form to provide feedback on their overall user experience
Notes: Similar to user study 2, the users were split into 2 groups: A and B
A performed the test using the qwerty keyboard first, ltnk second
B performed the test in the opposite order
Again, there were 2 phases: practice and test
For the test phase, sequence of characters follow a pattern of 5 keys that are far apart and 5 keys that were next to each other, alternating
After the tests, the participants had to fill up a Google Form to provide feedback on their overall user experience

## Slide 33
04 USER STUDIES
iii. LTNK KEYBOARD VS QWERTY KEYBOARD
RESULTS
Notes: These are the results of the user study.
The accuracy of achieved by the ltnk was higher, which matched the result of the 1st user study
Generally, it took longer for participants to type a character using the LTNK keyboard. This may be due to its hierarchical nature, which requires more keystrokes compared to the QWERTY keyboard. OR that users were more familiar with the qwerty keyboard.
However, the LTNK keyboard had a smaller standard deviation than the QWERTY keyboard, indicating that the time taken to select keys, whether close or far apart, was consistent on the LTNK keyboard, unlike the QWERTY keyboard.
This suggests that the LTNK keyboard may be more suitable for tasks that require precision and consistency, while the QWERTY keyboard may be more suitable for tasks that require speed and ease of use

## Slide 34
04 USER STUDIES
iii. LTNK KEYBOARD VS QWERTY KEYBOARD
Gaze Accuracy:
2.83/5 👎
Notes: The graph shows users’ perception of the accuracy of the gaze tracking.
The mean score calculated for the eye typing systems’ gaze accuracy was 2.83 out of 5
Participants perceived the gaze tracking accuracy to be inadequate

## Slide 35
04 USER STUDIES
iii. LTNK KEYBOARD VS QWERTY KEYBOARD
Dwell Time:
3.5/5 👍
Notes: The graph shows users’ perception of the dwell time.
The mean score calculated was 3.5 out of 5
Participants perceived the dwell time to be satisfactory.

## Slide 36
04 USER STUDIES
iii. LTNK KEYBOARD VS QWERTY KEYBOARD
Comfort:
2/5 👎
Notes: In terms of the comfortability of the eye typing setup:
Participants found it to be uncomfortable
In addition, participants provided comments such as:
“Neck was a little uncomfortable after putting my head on the rest for a while.”
“Eyes are tired from staring at the screen, neck was uncomfortable from resting on the
chin rest.”
“My eyes tired.”

## Slide 37
04 USER STUDIES
iii. LTNK KEYBOARD VS QWERTY KEYBOARD
Notes: All users preferred the ltnk keyboard over the qwerty keyboard
Users indicated:
LTNK keyboard had larger keys than the QWERTY keyboard, making it easier to accurately select the desired key.

## Slide 38
04 USER STUDIES
iii. LTNK KEYBOARD VS QWERTY KEYBOARD
Intuitiveness:
4.33/5 👍
Notes: In terms of intuitiveness, users generally found the ltnk keyboard to be easy to use.
Additionally, all participants responded “Yes” when asked if they could understand the functions of all the buttons, further supporting the keyboard’s perceived ease of use.

## Slide 39
04 USER STUDIES
iv. EFFECT OF REPEATED USE OF THE LTNK KEYBOARD ON TYPING SPEED
OBJECTIVES
  Determine whether repeated use of the LTNK keyboard will lead to faster typing speeds
METHODS
  Split into one practice phase and three test phases
  Each participant had to type the same set of 20 characters three times
Notes: From the results of user study 3, we know that the typing speed on the qwerty keyboard was faster. The last user study aims to determine if repeated use of the LTNK keyboard will lead to faster typing speeds.
For this experiment, users had to type the same set of characters three times, and their typing speeds were recorded and analysed.

## Slide 40
04 USER STUDIES
iv. EFFECT OF REPEATED USE OF THE LTNK KEYBOARD ON TYPING SPEED
RESULTS
Notes: These are the results.
In general, there is a decrease in the total time taken to type the same 20 characters. However, none of the total time reached that of the qwerty keyboard in user study 3
This shows that while repeated use of the ltnk keyboard could increase proficiency in using the keyboard, the qwerty keyboard is still better in terms of speed.

## Slide 41
04 USER STUDIES
DEMO
Notes: Before I move on to the conclusion, I would like to show a demonstration of eye typing on the LTNK keyboard

## Slide 42
05 CONCLUSION
  Higher accuracy than the QWERTY
  Typing speed is slower than QWERTY
  Repeated use LTNK led to faster typing speeds
    Did not surpass that of the QWERTY
  Participants favoured the LTNK over QWERTY
LTNK KEYBOARD
Notes: The results from user study 3 showed that while the LTNK keyboard had a higher accuracy than the QWERTY keyboard, typing speed was still slower than qwerty
User study 4 showed that typing speed could be improved from repeated use of the keyboard, but the results never surpassed that qwerty
User study 3 also showed that participants preferred LTNK keyboard over the QWERTY keyboard as the larger keys compensated for the inaccuracies in gaze estimation, making it easier to type.
Overall, ltnk keyboard is still a viable virtual keyboard option for eye typing.

## Slide 43
05 CONCLUSION
  Inaccurate gaze estimation
  Uncomfortable
  Can be improved by using deep learning
EYE TYPING SYSTEM
Notes: From user study 3, participants felt that the gaze tracking was overall inaccurate and that the eye typing setup was uncomfortable.
These issues can be improved by implementing more sophisticated gaze tracking methods, such as using deep learning, to remove the need for having a fixed head pose.

## Slide 44
THANK YOU